- Oxygenated VOCs as significant but varied contributors

- to VOC emissions from vehicles

- Sihang Wang1,2, Bin Yuan1,2,*, Caihong Wu1,2, Chaomin Wang1,2, Tiange Li1,2, Xianjun

- He1,2, Yibo Huangfu1,2, Jipeng Qi1,2, Xiao-Bbing Li1,2, Qing’e Sha1,2, Manni Zhu1,2,

- Shengrong Lou3, Hongli Wang3, Thomas Karl4, Martin Graus4, Zibing Yuan5*, Min

- Shao1,2

- 1 Institute for Environmental and Climate Research, Jinan University, Guangzhou

8	511443, China

9	2 Guangdong-Hongkong-Macau Joint Laboratory of Collaborative Innovation for

- Environmental Quality, Guangzhou 511443, China

- 3 State Environmental Protection Key Laboratory of Formation and Prevention of

- Urban Air Pollution Complex, Shanghai Academy of Environmental Sciences,

- Shanghai 200233, China

- 4 Department of Atmospheric and Cryospheric Sciences, University of Innsbruck,

- Innsbruck, Austria

- 5 College of Environment and Energy, South China University of Technology,

- University Town, Guangzhou 510006, China

18

19

- *Correspondence to: Bin Yuan (byuan@jnu.edu.cn) and Zibing Yuan

- (zibing@scut.edu.cn)

22

# Abstract:

- Vehicular emission is an important source for volatile organic compounds (VOCs)   in

- urban and downwind regions. In this study, we conducted a chassis dynamometer study

- to  investigate  VOC  emissions  from  vehicles  using  gasoline,  diesel,  and liquefied

- petroleum  gas  (LPG)  as  fuel.  Time-resolved  VOC  emissions  from  vehicles    are

- chemically	characterized	by	a	proton-transfer-reaction	time-of-flight	mass

- spectrometry (PTR-ToF-MS) with high frequency. Our results show that emission

- factors of VOCs generally decrease with the improvement of emission standard for

- gasoline  vehicles,  whereas  variations  of  emission  factors  for  diesel  vehicles with

- emission standards are more diverse. Mass spectra analysis of PTR-ToF-MS   suggest

- that cold start significantly influence VOCs emission of gasoline vehicles, while the

- influences are less important for diesel vehicles. Large differences of VOC  emissions

- between gasoline and diesel vehicles are observed with emission factors of most VOC

- species from diesel vehicles being higher than gasoline vehicles, especially for most

- oxygenated volatile organic compounds (OVOCs) and heavier aromatics. These results

- indicate  quantification  of  heavier  species  by  PTR-ToF-MS  may  be  important  in

- characterization of vehicular exhausts. Our results suggest that VOC pairs (e.g. C14

- aromatics/toluene ratio) could potentially provide good indicators for    distinguishing

- emissions from gasoline and diesel vehicles. The fractions of OVOCs in total VOC

- emissions are determined by combining measurements of hydrocarbons from canisters

- and online observations of PTR-ToF-MS. We show that OVOCs contribute 9.4% ± 5.6%

- of total VOC emissions for gasoline vehicles , while the fractions are significantly

- higher for diesel vehicles (52-71%), highlighting the importance to detect these OVOC

- species in diesel emissions. Our study demonstrated that the large number of    OVOC

- species measured by PTR-ToF-MS are important in characterization of VOC emissions

- from vehicles.

49

# 1.  Introduction

- Volatile  organic  compounds  (VOCs)  are  important  trace  components  in the

- troposphere, as important precursors of ground-level ozone (Shao et al., 2009) and

- secondary organic aerosol (SOA) (Seinfeld and Pandis, 2006;Kansal,    2009;Ziemann

- and Atkinson, 2012). As the result, it is particularly important to identify emission

- sources of VOCs in the atmosphere. Vehicular emission is an important source of VOCs

- in  cities  around  the  world  (Liu  et  al.,  2008;Parrish  et  al.,  2009),      contributing

- approximately  25%  of  total VOC  emissions  in  China  (Ou  et  al.,  2015;Wu  et al.,

- 2016;Sun  et  al.,  2018).  In  order  to  control  atmospheric  pollution  in  urban    and

- surrounding  regions,  it  is  necessary  to  understand  source  profiles  and   emission

- characteristics of VOCs from vehicles.

- Emissions  of  VOCs  from  vehicles  have  been  investigated  extensively from

- tunnel studies (Cui et al., 2018;Zhang et al., 2018;Song et al., 2020),    on-road mobile

- measurements (Li et al., 2017), and chassis dynamometer tests (Guo et al., 2011;Wang

- et al., 2013;Yang et al., 2018). Previous studies demonstrated that fuel types of vehicles

- strongly impact VOC emissions. Aromatics along with other hydrocarbons are known

- as compounds with high emissions in exhausts of gasoline vehicles (Wang et al.,

- 2013;Ly et al., 2020). Some carbonyl compounds contribute significantly to emissions

- of diesel vehicles, at fractions much higher than gasoline vehicles (Tsai et al., 2012;Qiao

- et al., 2012;Yao et al., 2015;Mo et al., 2016). Moreover, there are still a large   number

- of unidentifiable compounds in diesel vehicles (May et al., 2014). Furthermore,  VOC

- emissions from vehicles significantly decreased in China due to stricter emission

- standards (Liu et al., 2017;Sha et al., 2021). In order to reduce emissions of most

- primary pollutants, more stringent emission standards and after-treatment devices have

- been implemented. The emission standard of China VI has already been  implemented

- in July of 2019 in a few key cities in China and in July of 2021 nationwide. The emission

- limits for various air pollutants emitted by vehicles are significantly lower under the

- China VI emission standard (see details in the Supplement) (Wu et al., 2017). With the

- continuous development of engine and exhaust after-treatment technologies, emission

- characteristics of VOCs from vehicles may change and need to be frequently updated.

- Oxygenated volatile organic compounds (OVOCs) were found to be an important

- class of compounds in vehicle exhausts, accounting for more than 50% of the total VOC

- emissions  for  diesel  vehicles from  both  chassis  dynamometer  tests(Schauer  et al.,

- 1999;Mo  et  al.,  2016)  and  on-road  mobile  measurements  (Yao   et  al.,       2015).

- Traditionally, VOCs are collected in the canister or Tedlar bags, and then analyzed by

- gas   chromatography-mass   spectrometer/flame   ionization   detector (GC-MS/FID),

- mainly  reporting  emissions  of  hydrocarbons  (Wang  et  al.,  2017;Qi  et  al.,  2019).

- Previous work usually collected 2,4-dinitrophenyhydrazine (DNPH) cartridges and

- analyzed them using  high-performance  liquid  chromatography  (HPLC)  for      carbonyls

- (aldehydes and ketones), which are both time-consuming and prone to contaminations

90	(Mo et al., 2016;Han et al., 2019).

- The  large  variability  of VOC  emissions  under  different  engine  activities or

- driving  conditions  require  characterization  of  vehicular  emissions  at  higher  time

- resolution. Proton-transfer-reaction mass spectrometry (PTR-MS) has been used in   a

- number of studies for measurements of vehicle emissions. VOCs from vehicle exhausts

- under various driving and operational modes were measured by PTR-MS onboard a

- mobile laboratory (Zavala et al., 2006;Zavala et al., 2009). Drozd et al. (2016) used  a

- PTR-MS to emphasize the importance of cold start for vehicles, concluding that VOC

- emissions during cold start were equal to a 200 miles distance of driving during hot

- stabilized condition. Proton-transfer-reaction time-of-flight mass spectrometry  (PTR-

- ToF-MS)  can  provide  more  powerful  detection  of  various  VOCs,  thanks  to   the

- measurements  of  whole  mass  spectra  and  high  mass  resolution  (Cappellin  et al.,

- 2012;Yuan et al., 2017). More OVOC species could be quantified from the   measured

- mass  spectra  based  on  parameterization  methods  for  sensitivity  of       instrument

- (Sekimoto et al., 2017;Wu et al., 2020).

- In this study, we applied a PTR-ToF-MS along with a suite of other instruments

- to measure VOCs emitted from gasoline, diesel, and liquefied petroleum gas (LPG)

- vehicles. We  investigated  emission  factors  from  different  fuel  types  and emission

- standards for representative VOC species exhausted from these vehicles. We used  the

- dataset to  analyze  contributions  of various VOC  groups  to  total VOC emissions in

- different types of vehicles.

# 2.  Materials and methods

- 2.1 Tested vehicles and the chassis dynamometer study methods

- In this study, we conducted chassis dynamometer measurements to   investigate

- VOC emissions from vehicles using gasoline, diesel, LPG as fuel. All gasoline vehicles

- are light-duty-gasoline-vehicle (LDGV) with the emission standards from China I   to

- China VI, whereas diesel vehicles can be classified into light-duty-diesel-truck (LDDT),

- middle-duty-diesel-truck	(MDDT),	heavy-duty-diesel-truck	(HDDT),	and	bus

- associated with emission standards of China III to China V. In addition, the test vehicles

- using LPG are all taxis, which are under mandatory scrappage after 8 years of  driving

- in China; as a result only China IV and China V for LPG vehicles were   tested. After-

- treatment devices commonly used in light-duty gasoline vehicles are three-way catalyst

- (TWC)  and  gasoline  particulate  filter  (GPF)  (Lyu  et  al.,  2020).  These devices  have  been

- improved  with  the  stricter  emission  standards.  For  diesel  vehicles,  typical  after-

- treatment devices include diesel oxidation catalyst (DOC), diesel particulate filter

- (DPF), and selective catalyst reduction (SCR) (Zhou et al., 2019;Lyu et al., 2020;Shen

- et al., 2021). The diesel vehicles for China III or prior do not have any after-treatment

- devices. Light-duty-diesel-truck (LDDT) used DOC and DOC+DPF as after-treatment

- devices in China IV and V diesel vehicles, respectively. SCR devices are mainly used

- for heavy-duty-diesel-truck (HDDT) with China IV and V as after-treatment  devices.

- The fractions of gasoline and diesel vehicles with different emission standards in China

- are shown in Table S1 (MEEPRC, 2019;Li et al., 2021). Among the 38 vehicles we

- tested, a fraction of vehicles was measured several times, with a total of 62 experiments

- measured. The detailed information for test vehicles is summarized in Sect. 1 in the

- Supplement, Table S2 and Table S3.

- The short transient driving cycle (GB 18285-2018, Figure S1a), as one of the

- widely used test methods for vehicle emissions in China (Li et al., 2012;Wang et al.,

- 2013), was used for measurements of gasoline vehicles and LDDT, each running for

- three to five times. The short transient driving cycle methods were initially adapted

- based on emission regulations of the Economic Commission for Europe (ECE)   cycle

- (Yao et al., 2003), which is developed and used in European countries (Laurikko, 1995).

- The short transient driving cycle consist of four conditions, namely idling, acceleration,

- deceleration and uniform speed, as shown in Fig. S1. For the MDDT and HDDT,    we

- customized a step-by-step test method, in which the vehicle accelerates to 20   km·h-1,

- 40 km·h-1 and 60 km·h-1 in sequence after the engine activates, keeping at 20   km·h-1

- and 40 km·h-1 for 2 minutes, and 60 km·h-1 for 1 minute, respectively (Fig. S1) (Li  et

- al., 2021;Liu et al., 2021;Liao et al., 2021). In addition, the cold start was tested for   a

- number of vehicles after a cold soak for more than 12 hours at ambient temperature

- (20-25 ℃) before engine started. The measurements of cold start are compared to

- measurements of hot start after a ~10 minutes break for the vehicles after previous

- measurement. More details about cold start and hot start in this campaign can be found

- in Li et al. (2021).

- A custom-built sampling and dilution system for vehicles combining online and

- offline sampling techniques was used in this study. As shown in Fig. S2, a portable

- emission measurement system (PEMS, SEMTECH-DS, Sensors. USA) was employed

- to measure emissions of CO, CO2, NOX, and total hydrocarbon (THC) directly from the

- tailpipe of vehicles. A custom-built dilution system (Li et al., 2021;Liao et al.,   2021)

- was used for dilution of vehicular emissions, achieving dilution ratios of 10-100 for

- different  vehicles.  After  dilution,  CO2  and  CO  were  measured  using  a   Li-840A

- CO2/H2O Gas Analyzer (Licor, Inc. USA) and a Thermo 48i-TLE analyzer    (Thermo

- Fisher Scientific Inc. USA), respectively. Measurements of CO2 before and after    the

- dilution system was used to determine the dilution ratio for each test (see details in Fig.

162	S3).

# 2.2 VOC measurements using PTR-ToF-MS

- In this study, a Proton Transfer Reaction Quadrupole    interface Time-of-Flight

- Mass  Spectrometer  (PTR-QiToF-MS)  (Ionicon  Analytik,  Innsbruck,  Austria) with

- H3O+ chemistry was used to measure VOCs (Sulzer et al., 2014). The mass spectra  of

- PTR-ToF-MS was recorded every 1 s to capture characteristics of VOC species from

- vehicle  exhausts  in  real-time.  Background  measurements  of  the  instrument  were

- performed using sampled air through a custom-built platinum catalytical converter

- heated to 365 °C for 30 s before vehicle starts in each test. The more detailed setting

- parameters for the instrument can be found elsewhere (Wu et al., 2020;Wang et al.,

- 2020a;He et al., 2022). Data analysis of PTR-ToF-MS was performed using the Tofware

- software package (version 3.0.3, Tofwerk AG, Switzerland) (Stark et al., 2015).

- A 23-component gas standard (Linde Spectra) was used for daily calibration  of

- PTR-ToF-MS during the campaign. VOC sensitivities from automatical    calibrations

- indicated quite stable instrumental performance for most of the VOC species (Fig. S4).

- Another gas standard with 35-component VOCs (Apel Riemer Environmental Inc.) was

- used for calibrations during the later period of this campaign to include more VOC

- species  in  the  calibration.  The  Liquid  Calibration  Unit  (LCU,  Ionicon   Analytik,

- Innsbruck, Austria) was used to calibrate a total of 11 organic acids and nitrogen-

- containing species (Table S4). The limits of detection for calibrated VOC species   are

- below 100 ppt for the 1-s measurement, except for ethanol (423 ppt) and formic   acid

- (166 ppt). Additionally, the humidity dependence for a few VOC species in PTR-ToF-

- MS (Yuan  et al., 2017;Koss et al., 2018) were corrected using    humidity-dependence

- curves determined in the laboratory, as previously shown in Wu et al. (2020). To

- quantify the ion signals without calibration, we determine the sensitivities based on the

- kinetics   of   proton-transfer   reactions   of   H3O+   with   VOCs   (Cappellin   et   al.,

- 2012;Sekimoto et al., 2017). The relationship between VOCs sensitivity and kinetic

- rate constants for the same instrument has been reported in Wu et al. (2020) and He et

- al. (2022). The corrected sensitivities as a function of kinetic rate constants for proton-

- transfer reactions of H3O+ with VOCs during this campaign is shown in Fig. S5.   The

- fitted line is used to determine sensitivities of uncalibrated species, and the uncertainty

- of the concentrations for uncalibrated species are determined to be around 50%.

# 2.3 Other VOC measurements

- Whole air samples were collected using canisters after the dilution system for

- determination of hydrocarbons emitted from various vehicles. All the canisters    were

- sent to the laboratory for analysis by an offline GC-MS/FID system, with a total 95

- hydrocarbons calibrated by Photochemical Assessment Monitoring Stations   (PAMS)

- and TO-15 standard mixtures (Table S5). We  compared emission factors from    PTR-

- ToF-MS   and  the  offline  canister-GC-MS/FID  (Fig.  S6c-d),  obtaining     generally

- consistent  results,  considering  the  large  variation  of  VOC  emissions  for   driving

- conditions and the difficulty to control the fill time for canisters.

- An  instrument  based  on  Hantzsch  reaction-absorption  method  was  used to

- measure formaldehyde (Zhu et al., 2020). Good agreement for formaldehyde  between

- PTR-ToF-MS and the Hantzsch instrument was obtained (Fig. S6a). An iodide-adduct

- time-of-flight   chemical   ionization   mass   spectrometer   (I-   ToF-CIMS, Aerodyne

- Research, Inc.) (Wang et al., 2020c;Ye et al., 2021) was used to measure organic acids,

- hydrogen cyanide (HCN), and isocyanic acid (HNCO) from vehicles (Li et al.,  2021).

- As shown in Fig. S6b, formic acid measured by PTR-ToF-MS and I- ToF-CIMS showed

- reasonable agreement.

# 2.4 Emission factors and emission ratios calculation

- In this study, we determine emission factors of VOC species in two different

- approaches: the mileage-based emission factors (mg·km-1) as the mass of these VOCs

- exhausted per kilometer driving of vehicles, and the fuel-based emission factors

- (mg·kgfuel-1) as the mass of VOCs per kilogram of fuel burned by the vehicles. In

- addition, emission ratios of VOCs to combustion tracers (usually CO) are widely

- applied in vehicle emissions in urban regions, as the result we determine emission

- ratios to CO in ppb·ppm-1 as well. More details about the determination of  emission

- factors and emission ratios can be found in Sect. 2 in the Supplement.

- The average emission factors for various types of vehicles are determined from

- arithmetic means for different emission standards of vehicles. As for diesel  vehicles,

- the average emission factors are obtained from the arithmetic means of LDDT, MDDT,

- HDDT, and bus. Besides, we also calculate emission factors and emission ratios from

- weighted means based on the fractions of gasoline and diesel vehicles with  different

- emission standards in China (MEEPRC, 2019;Li et al., 2021) (see Sect. 2 in the

- Supplement for details). In order to evaluate the uncertainties of obtained emission

- factors, the average limit of detection for VOC species are used to estimate the  limit

- of detection for the determined emission factors (more details can be found in Sect. 3

- in the Supplement).

# 3.  Results and discussions

- 3.1 Characteristics of the VOC emissions in the vehicles

- Time series of several aromatics and OVOC species measured by PTR-ToF-MS

- for a selected gasoline vehicle associated with emission standard of China I and a LDDT

- associated with China IV emission standard are shown in Fig. 1. Both tests started with

- cold engines of the two vehicles. Benzene and toluene are typical aromatic species

- emitted by vehicles. As shown in Fig. 1a, high concentrations of benzene and  toluene

- exhausted  by  the  gasoline  vehicle  were  observed  as  the  engine  started.  The

- concentrations of the two species continued to increase until ~2 min after the engine

- started, and then  dropped  rapidly before  a minor  increase  during the    acceleration

- condition.  These  observations  are  similar  to  the  previous  results  from   PTR-MS

- measurements in Drozd et al. (2016). Acetaldehyde and acetone are important OVOC

- species emitted from vehicles. They show similar temporal variations as benzene  and

- toluene. However, concentrations of acetaldehyde and acetone were much lower  than

- the two aromatics after engine started. Compared to the concentrations at engine start-

- up for the gasoline vehicle (the first cycle), concentrations of the VOCs are 3.0 to   40

- times lower during the gasoline vehicle running at hot stabilized condition (the third

- cycle). As shown in Fig. 1 for the diesel vehicle, enhanced emissions from cold start

- are minor, which is different from the gasoline vehicle. The concentration of these

- VOCs at engine start-up for the diesel vehicle are only 1.3 to 2.5 times higher than the

- periods as the diesel vehicle running at hot stabilized condition. It indicates that the

- impact  of  the  engine  start-up on  emissions in  diesel  vehicles    is  much lower than

- gasoline  vehicles.  This may be explained by  a  combined  effect  of  cold  engine  and    operation

- temperature of the after-treatment device (Gentner et al., 2017;George et al., 2015). In

- contrast to the gasoline vehicle, we observe higher concentrations of the two OVOC

- species than the two aromatics species, namely benzene and tolune,from the diesel vehicle. These higher OVOC

- concentrations in diesel vehicle exhausts are in line with the higher observations of organic

- acids using the I- ToF-CIMS from the same campaign (Li et al., 2021).

- Based   on   the   high   time-resolution   measurements   of   PTR-ToF-MS,  we

- determined emission factors of various VOC species from different vehicles. Fig. 2

- shows  the  determined average mileage-based  emission  factors  of benzene, toluene,

- acetaldehyde,  and  acetone  for  various  types  of  vehicles  (also  tabulated  in      the

- Supplement table). In general, we observe a downward trend for emissions factors   of

- gasoline  vehicles  from  China  I  to  China  VI  emission  standards  for  the  four

- representative VOC species. This is consistent with the results in previous studies with

- lower emissions for newer emission standards (Wang et al., 2017;Sha et al., 2021).  In

- addition, the dependence of VOCs emission versus emission standard may also be

- attributed to the history of vehicle usage, i.e., the mileage traveled by the vehicles,   as

- lower mileages of vehicles are usually associated with vehicles with newer emission

- standards. As shown in Fig. 3, we observe strong positive relationship between toluene

- emission factors and vehicle odometers for both gasoline and diesel vehicles, indicating

- the mileages of vehicles can significantly affect VOCs emission factors for vehicles

- tested in this study. The emission factors of the representative VOC species are highest

- for China II gasoline vehicles rather than China I vehicles, which can be explained by

- the China II vehicles having the highest mileage of the test vehicles.Intestinally, the

- emission factors of the representative VOC species are highest for China II gasoline

- vehicles rather than China I vehicles, coincidence with largest mileage of the test

- vehicles. Emission factors of the four species for China VI vehicles are 12 to 25 times

- lower than emission factors for China I vehicles, indicating that newer emission standards

- successfully reduced VOC emissions of gasoline vehicles. The decline of emission

- factors for the four species with newer emission standards for diesel vehicles are in the

- range of 1.1 to 7.4 times from China III to China V,  compared to 4.5 to 5.4 times

- reduction from China III to China V for gasoline vehicles. Emission factors of benzene

- and toluene from diesel vehicles are in the range of 0.8 to 7.4 mg·km-1 and 0.3 to   5.8

- mg·km-1, which are comparable to emission factors from gasoline vehicles with China

- IV to China VI emission standards. This is different from observations of the two

- OVOC species (acetaldehyde and acetone), with much higher emission factors    from

- diesel vehicles (8.0 to 27.9 mg·km-1 for acetaldehyde and 0.8 to 10.0 mg·km-1 for

- acetone) than almost all gasoline vehicles (a maximum of 3.9 mg·km-1 for acetaldehyde

- and a maximum of 3.2 mg·km-1 for acetone). Higher emission factors from diesel

- vehicles are also observed for many other common OVOC species, as shown in Fig. 4.

- As the largest OVOCs emitted from gasoline vehicles (4.6 ± 5.1 mg·km-1), methanol is

- found to be the only common OVOC species with lower emission factors from diesel

- vehicles   than   gasoline   vehicles.   The   emission   factor   of   other   OVOCs  (e.g.

- formaldehyde, acetone) from diesel vehicles are higher than gasoline vehicles,   which

- is consistent with previous results (Gentner et al., 2013). The high emissions of OVOCs

- from diesel vehicles may be related to combustion processes in diesel vehicles, with

- more excess air present in the combustion cylinder (i.e., overall fuel-lean conditions)

- resulting  in  higher  oxygen  contents  and  more  oxidation  processes  during      fuel

- combustion (Pang et al., 2008;Qiao et al., 2012;Gentner et al., 2017). Finally, the

- determined emission factors of the four VOC species from LPG vehicles are much

- lower than both gasoline and diesel vehicles.

# 3.2 Analysis	of	PTR-ToF-MS	mass	spectra	to	evaluate	VOCs

- speciation

- In  addition  to  typical  VOC  species  shown  above,  PTR-ToF-MS    detected

- abundant signals for a large number of ions. The determined average mileage-based

- emission factors for all detected VOC species are shown as mass spectra in Fig. 4. VOC

- species measured by PTR-ToF-MS were divided into groups according to chemical

- formula, namely hydrocarbon species only containing C and H atoms (CxHy), OVOCs

- (CxHyOz), species containing nitrogen and/or sulfur atoms (N/S-containing), and some

- other ions (others). We  observe similar mass spectra of emission factors for   gasoline

- vehicles with different emission standards (Fig. S7). Highest emission factors from

- gasoline vehicles (Fig. 5a) are detected as hydrocarbons, including C6 to C10 aromatics.

- A few OVOC species, namely methanol, ethanol, formaldehyde, acetaldehyde and

- acetone, are also observed as the largest emissions. In contrast to gasoline vehicles, the

- largest emissions from diesel vehicles were attributed to a few  low-molecular-weight

- OVOC species, including formaldehyde, acetaldehyde, formic acid, and acetic acid,

- followed by a large number of hydrocarbon species. Comparison between the mass

- spectra of gasoline and diesel vehicle emissions suggest that emissions from diesel

- vehicles are more evenly distributed among different VOC species, as reflected by  50

- and 140 species contributing more than 1‰ of the total emissions for gasoline and diesel

- vehicles, respectively. As shown in Fig. 5b, many hydrocarbon ions in the range of m/z

- 150-200  still  account  for  significant  fractions  of  emissions  from  diesel  vehicles,

- whereas only one species in this m/z range contribute more than 1‰ of emissions from

- gasoline vehicles. These results demonstrate that diesel vehicles emit more heavier

- hydrocarbons than those from gasoline vehicles, which is consistent with observations

- in previous studies (Gentner et al., 2012;Erickson et al., 2014). It should be noted that

- the signals of C16H22O4H (m/z=279) were higher during the tests based on determined

- emission  factors.  However,  we  suspect  that  it  may  be  emitted  artifacts  from the

- sampling or dilution system as it mainly showed higher signals in the latter period   of

- each test when sampling materials absorb more heat from vehicle exhausts (Fig.   S8),

- and thus it is not included in Fig. 5 (details in the Sect. 3 in the Supplement).

- The scatterplot of carbon oxidation states (-𝑂--𝑆-C-) as a function of carbon number

- (𝑛C) provides a framework for describing bulk chemical properties of organics  (Kroll

- et al., 2011). The details of -𝑂--𝑆-C- calculation is included in Sect. 4 in the Supplement.

- The results from gasoline and diesel vehicles are compared in Fig. 6 (LPG vehicles are

- shown in Fig. S89). It is apparent that ions with carbon oxidation states between -2.0 to

- 0 comprise main emissions for each carbon number for both gasoline and diesel

- vehicles. It is interesting to observe that averaged -𝑂--𝑆-C- for 𝑛C>6 increase as the carbon

- number decrease for both gasoline and diesel vehicles, whereas the opposite trends are

- observed  for 𝑛C<5. The  averaged -𝑂--𝑆-C- in  diesel  vehicles  for 𝑛C between 1 and 5 are

- significantly higher than those in gasoline vehicles, as the result of high emissions   of

- C2 to C5 low-molecular-weight OVOCs. Fig. 6c further shows that emission factors of

- most VOC species from diesel vehicles were higher than gasoline vehicles, except for a

- number of species occupying the right-bottom corner of the two-dimensional space.

- The determined mass spectra of PTR-ToF-MS in terms of emission factor for

- different types of vehicles can be used to explore the dependence of various VOC

- emissions to different factors. Fig. 7a-b shows scatterplots of the average mileage-

- based emission factors of VOCs between cold start and hot start for gasoline and diesel

- vehicles, respectively. We observe strong correlation between emission factors   from

- cold start and hot start tests (R=0.99 and 0.92) and generally consistent ratios between

- cold start and hot start for different types of VOC species for both gasoline and diesel

- vehicles, indicating that variation behaviors are similar for different species and thus

- chemical  compositions  of VOC  emissions  are  comparable  between  different start

- conditions. As cold start emissions are richer in unburned fuel than other hot-running

- conditions (Gentner et al., 2017) and the after-treatment devices aim for VOCs control

- for gasoline vehicles, the strong correlation and significantly lower than unity slope in

- Fig. 7a, the observation in Fig. 7a-b also suggest that unburned fuel are the major

- contributor  for  vehicle  exhaust  emissions  of  gasoline  vehicles,  which  has   been

- previously shown in California, U.S. (Gentner et al., 2013). It is obvious that emission

- factors of VOCs during cold start are significantly higher than those during hot   start

- for gasoline vehicles (slope=0.40), whereas similar emissions factors between cold

- start and hot start are derived for diesel vehicles (slope=0.84). These results   suggest

- that gasoline vehicles are more significantly influenced by cold start, as the result  of

- compositions in gasoline fuel being more volatile than diesel fuel (US NRC, 1996). We

- further  explore  the  effects  of  emission  standards  on  VOC  emission  factors   by

- comparing determined emission factors between China I and China V for gasoline

- vehicle (Fig. 7c, also see China III versus China V and China V versus China VI in

- Fig. S910) and between China III and China V for LDDT (Fig. 7d, also see China III

- versus China V for MDDT and HDDT in Fig. S910). Fig. 7c-d show that the chemical

- compositions of VOC emissions are comparable between different emission standards

- for abundant VOC species from gasoline vehicles, both gasoline and diesel  vehicles

- (R=0.98 and 0.89), indicating after-treatment devices may not affect the relative

- fractions of VOC components for gasoline vehicles (Drozd et al., 2019;Lu et al.,

- 2018;Zhao  et  al.,  2017).  In  comparison,  the  results  between  different   emission

- standards for diesel vehicles (Fig. 7d) are somewhat more scattered than in gasoline  vehicles.

- Furthermore, comparison of both gasoline and diesel vehicles demonstrate newer

- emission  standards  successfully  decreased  VOC  emissions. Based  on  the derived

- slopes, we obtain VOCs emission factors that are reduced by a factor of 10 for gasoline

- vehicles from China I to China V (a factor of 5 reduction from China III to China  V

- and a factor of 2.5 reduction for China V to China VI), and a factor of 2 for

- LDDT from China III to China V (a factor of 1.5 and 8 reduction for MDDT and

- HDDT from China III to China V). The reduction ratio for gasoline vehicles from

- China I to China V are generally similar for most VOC species, except that some

- OVOC species showed smaller reduction ratios. The reduction ratios for LDDT vehicles

- from China III to China V show large variability for different species. The lowest

- reduction ratios (a factor of ~2) are observed for the low-molecular weight OVOC

- species associated with largest emissions, while the reduction ratios for hydrocarbons

- and higher-molecular weight OVOCs are in the range of a factor of 10-100. These

- results  indicate  the  after-treatment  device  for  diesel  vehicles  (see  Sect.  1  in the

- Supplement for details.) may effectively reduce emissions of some heavier VOC

- species, though the after-treatment devices do not aim for VOCs control (Gentner  et

392	al., 2017).

# 3.3 Non-target analysis for comparison between gasoline and     diesel

- vehicles

- As shown in the previous section, the analysis of PTR-ToF-MS mass spectra

- provide rich information on understanding the influences of VOC emissions from

- vehicles.  This  detailed  information  provided  by  the  PTR-ToF-MS  also  offer  an

- opportunity to systematically compare emissions between gasoline and diesel vehicles.

- The scatterplot of the determined average emission factors of various VOC species

- between gasoline and diesel vehicles is shown in Fig. 8. Large differences in VOC

- compositions emitted from gasoline and diesel vehicles are observed, as indicated by

- the low correlation of the data points (R=0.24). A limited number of VOC species,

- including  C6-C10  aromatics  and  some  N/S-containing  species  (e.g.  C7H5N)    are

- associated with higher emission factors from gasoline vehicles, whereas the obtained

- emission  factors  of  most  VOC  species  emitted  from  diesel  vehicles  are higher,

- especially for most OVOC species. For example, formic acid is found to be one of the

- most significant  species emitted by  diesel vehicles, with emission factors being three orders

- of magnitude higher than those from gasoline vehicles. In addition, emission factors of

- HCN from gasoline vehicles are similar to those from diesel vehicles. These   results

- are consistent with the measurements using the I- ToF-CIMS from the same campaign,

- as shown in Li et al. (2021).

- The scatterplot shown in Fig. 8 can also be expressed in terms of the determined

- fuel-based  emission  factors  between  gasoline  and  diesel  vehicles  (Fig.   S101a).

- Generally, similar variability is obtained except the determined slope of the data points,

- with higher slopes determined from the scatterplot based on fuel-based emission factor

- (0.19 versus 0.15). The emission ratios to CO between gasoline and diesel vehicles

- (Fig. S101b) show similar results. Furthermore, the difference between the slopes

- reflects the different average mileage for the same weight of fuel between gasoline

- (9.7 km·kgfuel  ) and diesel vehicles (7.1 km·kgfuel  ), as demonstrated for emission

- factors of CO2 in Table S6.

- Comparing  gasoline  and  diesel  vehicles,  we  can  also  observe       profound

- differences in relative changes of emission factors for analogous compounds series. The

- emission factors of C6-C10 aromatics are apparently higher for gasoline vehicles   than

- diesel vehicles, whereas emission factors for larger aromatics (𝑛C>11) from diesel

- vehicles start to exceed gasoline vehicles. This interesting behavior is the result of

- different  variations  of emission factors  for  gasoline  and diesel  vehicles  as  carbon

- number increases. This may be attributed to the differences of chemical  compositions

- of  gasoline  and  diesel  fuel,  such  as  higher  fractions  of  polycyclic  aromatic

- hydrocarbons (PAHs) in the diesel fuel (Yue et al., 2015;Gentner et al., 2017). As shown

- in Fig. 9, emission factors of aromatics from gasoline vehicles start to rapidly decrease

- at 𝑛C=10 (a factor of 5 for each additional carbon for C10-C15), while the emission

- factors of aromatic for diesel vehicles demonstrate a relatively flat pattern between C6

- and C15, only with significant decrease for 𝑛C>15. Based on Fig. 9, we determine that

- emissions of aromatics with 𝑛C≥10 in gasoline and diesel vehicles account for 14%

- and 63% of total aromatic emissions, respectively, again suggesting the importance of heavier aromatics

- in emissions from diesel vehicles. It also highlights that quantification of these heavier

- species by PTR-ToF-MS may be important in characterization of vehicular   exhausts,

- especially diesel vehicles.

- In addition to aromatics, the relative changes of emission factors for   carbonyls

- with carbon number are apparently different between gasoline and diesel vehicles (Fig.

- 8 and Fig. 9b). Emission factors of carbonyls tend to decrease as carbon number

- increases for both gasoline and diesel vehicles. The extent of this decrease is observed

- to be comparable for C1-C6 carbonyls in gasoline (97.6%) and diesel vehicles

- (97.4%). However, as 𝑛C>6, the decrease in carbonyl emission factors for diesel

- vehicles become smaller, resulting in larger emissions factors than gasoline vehicles  for

- this range of carbon number.

- The above discussions demonstrate that emission characteristics of aromatics and

- OVOCs are significantly different between gasoline and diesel vehicles. As the result,

- the ratios of VOC pairs can be used to distinguish emissions of gasoline and diesel

- vehicles. Fig. 10 shows the scatterplots of four representative VOCs (benzene, C14

- aromatics, formaldehyde, and acetaldehyde) versus toluene based on the  determined

- emission factors. The data points for each VOCs pair clearly show distinct separation

- between gasoline vehicles and diesel vehicles, with apparently higher slopes for diesel

- vehicles than gasoline vehicles, as the result of much larger emission factors of toluene

- from gasoline vehicles and lower emission factors of the four representative VOCs

- from diesel vehicles. The benzene/toluene ratio in gasoline and diesel vehicle are

- determined as 0.48 and 1.24 mg·mg-1 (corresponding to 0.57 and 1.46 ppb·ppb-1 that

- are more widely used in ambient studies). The difference of benzene/toluene ratio

- between gasoline and diesel vehicles has been reported in previous studies, and    our

- results are generally consistent with these previous results (Chan et al., 2002;Barletta

- et al., 2005;Qiao et al., 2012;Kumar et al., 2020). Compared to benzene/toluene ratio,

- the difference of C14 aromatics/toluene ratio between gasoline and diesel vehicles are

- more substantial (a factor of 3800). The significantly higher emission factors of   C14

- aromatics from diesel vehicles suggest that diesel vehicles can be a significant or even

- dominant  source  of  higher  molecular-weight  aromatics.The  remarkable     larger

- emission factors of C14 aromatics from diesel vehicles suggest that diesel vehicles can

- be a significant or even predominated source for higher molecular aromatics. The

- enormous   difference   of   C14   aromatics/toluene   ratio   (and   also   other   higher

- aromatics/toluene) between gasoline and diesel vehicles indicate these ratios could

- potentially provide good indicators for separation of gasoline and diesel vehicles    in

- ambient or tunnel studies (see discussion in Sect. 5 in the Supplement for details about

- the feasibility of the ratio using in ambient air). Similar discrepancies are observed for

- formaldehyde/toluene and acetaldehyde/toluene ratios between gasoline and     diesel

- vehicles. These ratios may not be able to be used as indicators to distinguish gasoline

- and diesel vehicles in ambient studies, since secondary sources may complicate the

- observed ratios in ambient air. However, these results strongly suggest that diesel

- vehicles can be important in emissions of these OVOC species, though the number of

- diesel vehicles are smaller than gasoline vehicles in many countries, e.g. China and

- U.S (Wallington et al., 2013;Yao et al., 2015;Huang et al., 2021).

# 3.4 OVOC fractions in VOC emissions

- Emission  factors  of  various  VOC  species  measured  by  PTR-ToF-MS from

- different vehicles are summarized in Fig. 11. As shown in Fig. 11a, the determined

- average mileage-based emission factors of total VOC ions from diesel vehicles    were

- much higher than gasoline and LPG vehicles. Fig. 11b-d quantified the proportions of

- different  categories  of  ions  measured  by  PTR-ToF-MS.  The  determined  average

- mileage-based emission factors of CxHy accounted for the largest fraction in  gasoline

- vehicles (84% ± 5.9%), and lower fractions in diesel (47% ± 16%) and LPG   vehicles

- (32% ± 0.7%). OVOCs account for larger fractions in diesel (49% ± 16%) and LPG

- vehicles (58% ± 3.7%), while they only account for 13% ± 6.1% of emissions from

- gasoline vehicles. The fractions of different OVOC groups generally demonstrate a

- downward trend from CxHyO1 to CxHyO≥3, and OVOCs with more than two oxygen

- atoms  only  occupy  small  percentages  (0-7%)  in  vehicle  exhausts,  indicating low

- emissions of these species.

- Combined with measurements of other VOCs from canisters measured by  GC-

- MS/FID,  the  fractions  of  OVOCs  in  total VOC  emissions  can  be  determined for

- different vehicles (details in Sect. 6 in the Supplement) (Fig. 12). OVOCs account  for

- 9.4% ± 5.6% of total VOC emissions for gasoline vehicles. The OVOC fractions   for

- gasoline  vehicles  are  generally  comparable  for  different  emission  standards   and

- cold/hot start, except somewhat higher fractions for China VI from hot start (Fig. S112).

- The  OVOC  fractions  obtained  in  this  study  for  gasoline  vehicles  are    generally

- consistent with previous results (Cao et al., 2016;Wang et al., 2020b) (Fig. 12). Among

- these studies, the OVOC fractions determined for gasoline with 10% ethanol (E10)

- (Roy et al., 2016) (22% ± 11%) are apparently higher. The fractions of OVOCs in total

- VOC emissions for diesel vehicles are 71% ± 20%, 65% ± 22%, 52% ± 18%, and 56%

- ± 26% for LDDT, MDDT, HDDT, and bus, respectively. The variations of OVOC

- fractions with emission standards are observed to be mixed among different types    of

- diesel vehicles (Fig. S112). The OVOC fractions from diesel vehicles are obviously

- higher than those in gasoline vehicles, indicating the importance of OVOCs    in VOC

- emissions from diesel vehicles. Compared to previous studies (Tsai et al., 2012;Qiao   et

- al., 2012;Cao et al., 2016;Mo et al., 2016), determined OVOC fractions for diesel

- vehicles in this study are higher. If only considering carbonyls among various types of

- OVOCs measured by PTR-ToF-MS, the OVOC fractions determined in this study are

- more comparable with previous studies (Fig. 12), since most previous studies only

- detected carbonyls among various types of OVOCs. Finally, we determine that OVOCs

- account for 41% ± 10% of total VOC emissions for LPG vehicles, which is also higher

- than  a  previous  study  (Wang  et  al.,  2020b)  where  only  carbonyls  and  a few

- esters/alcohols were included. These results stress that the large number of OVOCs measured

- by PTR-ToF-MS are important in characterization of VOC emissions from vehicles. It

- should be noted that the OVOC fractions obtained here only reflect exhaust emissions.

- Evaporative emissions may also be associated with different fractions of various VOC

- groups, which may be more related to fuel compositions (Rubin et al., 2006;Huang  et

522	al., 2021).

# 4.  Conclusions

- In  this  work,  we  conducted  a  chassis  dynamometer  study  to measure VOC

- emissions from gasoline, diesel, and LPG vehicles using PTR-ToF-MS along with other

- offline and online measurement techniques. Using this dataset, we provide emission

- factors of many VOCs from these three different types of vehicles associated with

- various emission standards in China. Our results show that emission factors of  VOCs

- generally decrease with the increased stringency of emission standards for gasoline

- vehicles, whereas variations of emission factors for diesel vehicles with emission

- standards are more diverse. Mass spectra analysis of PTR-ToF-MS suggest that    cold

- start significantly influence VOCs emission of gasoline vehicles, while the  influences

- are smaller for diesel vehicles.

- We observe large differences of VOC emissions between gasoline and diesel

- vehicles based on PTR-ToF-MS measurements. Emission factors of most VOC species

- from diesel vehicles were higher than gasoline vehicles, especially for most    OVOCs

- and  heavier  aromatics. The  substantially  larger  emission  factors  of  some OVOCs

- emission factors for diesel vehicles indicate potentially dominant emissions of these

- species from diesel vehicles among vehicular emissions. Our results suggest that VOC

- pairs (e.g. C14 aromatics/toluene ratio) could potentially provide good indicators for

- distinguishing emissions between gasoline and diesel vehicles.

- Based on measurements of PTR-ToF-MS, CxHy ions account for the largest

- fraction  in  gasoline  vehicles  (84%  ±  5.9%),  whereas  OVOC  ions  are  the largest

- contributor in the mass spectra of emissions from diesel (49% ± 16%) and LPG vehicles

- (58%  ±  3.7%).  In  the  end,  the  fractions  of  OVOCs  in  total  VOC  emissions are

- determined by combining hydrocarbons measurements from canister results and online

- measurements of PTR-ToF-MS. We show that OVOCs contribute 9.4% ± 5.6% of

- the  total VOC  emissions from gasoline  vehicles  ,  while  the fractions are significantly

- higher for diesel vehicles (52-71%), highlighting the importance to measure these OVOC

- species in diesel emissions.

- This study shows significant contributions of OVOCs in VOC emissions    from

- various vehicles, especially diesel vehicles. As a consequence, vehicular emissions may

- account for considerable proportions for primary emissions of these OVOCs in  urban

- regions.  Emissions  of  many  OVOC  species  are  currently  not  fully represented in

- emission inventories of VOCs, which may in turn affect the prediction ability of air

- quality models in urban regions. In this study, OVOC species are mainly quantified

- from PTR-ToF-MS measurements by taking into account all signals in the mass spectra,

- which stress that the large number of OVOC species measured by PTR-ToF-MS are

- important in characterization of VOC emissions from vehicles.

# Data availability

- Data are available from the authors upon request.

# Author contribution

- BY designed the research. ZBY, BY, QES organized vehicle test measurements.

- SHW, CHW, CMW, TGL, JPQ, QES, and MMZ contributed to data collection.   SHW

- performed the data analysis, with contributions from TGL, XJH, YBH, XBL, and QES.

- SHW and BY prepared the manuscript with contributions from other authors. All   the

- authors reviewed the manuscript.

# Competing interests

- The authors declare that they have no known competing financial interests or

- personal relationships that could have appeared to influence the work reported in  this

- paper.

# Acknowledgement

- This work was supported by the National Key R&D Plan of China (grant No.

- 2019YFE0106300, 2018YFC0213904), the National Natural Science Foundation    of

- China  (grant  No.  41877302,  42121004),  Guangdong  Natural  Science  Funds    for

- Distinguished Young  Scholar  (grant  No.  2018B030306037),  Guangdong  Basic and

- Applied Basic Research Fund Project (grant No. 2020A1515110085), and Guangdong

- Innovative and Entrepreneurial Research Team Program (grant No.  2016ZT06N263).

- This work was also supported by Special Fund Project for Science and Technology

- Innovation Strategy of Guangdong Province (Grant No.2019B121205004). TK and

- MG were supported by OEAD grant CN 05/2020. The authors would like to thank Prof.

- Junyu Zheng for providing many resources during vehicle measurements and allowing

- to use PEMS and formaldehyde data in this study.

# References

- Permissible  Exposure  Levels  for  Selected  Military  Fuel  Vapors,  The      National

- Academies Press, Washington, DC, 1996.

- Barletta, B., Meinardi, S., Sherwood Rowland, F., Chan, C.-Y., Wang, X., Zou, S., Yin

- Chan,  L.,  and  Blake,  D.  R.:  Volatile  organic  compounds  in  43  Chinese     cities,

590      Atmospheric Environment, 39, 5979-5990, 10.1016/j.atmosenv.2005.06.029, 2005.

591       Cao, X., Yao, Z., Shen, X., Ye, Y.,  and Jiang, X.: On-road emission characteristics   of

592      VOCs from light-duty gasoline vehicles in Beijing, China, Atmospheric Environment,

593      124, 146-155, 10.1016/j.atmosenv.2015.06.019, 2016.

594      Cappellin, L., Karl, T., Probst, M., Ismailova, O., Winkler, P. M., Soukoulis, C., Aprea,

595       E., Mark, T. D., Gasperi, F., and Biasioli, F.: On quantitative determination of  volatile

596           organic compound concentrations using proton transfer reaction time-of-flight mass

597       spectrometry,      Environmental      Science      &      Technology,      46,    2283-2290,

598       10.1021/es203985t, 2012.

599  Chan, C. Y., Chan, L. Y., Wang, X. M., Liu, Y. M., Lee, S. C., Zou, S. C., Sheng, G. Y., 600   and  Fu,  J.  M.:  Volatile  organic  compounds  in  roadside  microenvironments  of    601    metropolitan    Hong    Kong,     Atmospheric     Environment,     36,     2039-2047,    602       https://doi.org/10.1016/S1352-2310(02)00097-3, 2002.

603       Cui, L., Wang, X. L., Ho, K. F., Gao, Y., Liu, C., Hang Ho, S. S., Li, H. W., Lee, S. C.,

604    Wang, X. M., Jiang, B. Q., Huang, Y.,  Chow, J. C., Watson, J. G., and Chen, L.-W.:     605 Decrease of VOC emissions from vehicular emissions in Hong Kong from 2003 to 2015: 606    Results    from     a     tunnel     study,    Atmospheric     Environment,     177,     64-74, 607      10.1016/j.atmosenv.2018.01.020, 2018.

608  Drozd, G. T., Zhao, Y., Saliba, G., Frodin, B., Maddox, C., Weber, R. J., Chang, M. O., 609  Maldonado,  H.,  Sardar,  S.,  Robinson, A.  L.,  and  Goldstein, A.  H.: Time  Resolved 610 Measurements  of  Speciated Tailpipe  Emissions  from  Motor Vehicles:  Trends  with 611  Emission  Control  Technology,  Cold  Start  Effects,  and  Speciation,  Environmental 612       Science & Technology, 50, 13592-13599, 10.1021/acs.est.6b04513, 2016.

613      Drozd, G. T.,  Zhao, Y.,  Saliba, G., Frodin, B., Maddox, C., Oliver Chang, M. C.,      614 Maldonado, H., Sardar, S., Weber, R. J., Robinson, A. L., and Goldstein, A. H.: Detailed 615  Speciation of Intermediate Volatility and Semivolatile Organic Compound Emissions  616 from Gasoline Vehicles: Effects of Cold-Starts and Implications for Secondary Organic 617      Aerosol  Formation,  Environ  Sci Technol,  53,  1706-1714, 10.1021/acs.est.8b05600,

618      2019.

619   Erickson, M. H., Gueneron, M., and Jobson, B. T.:  Measuring long chain alkanes in   620 diesel  engine  exhaust  by  thermal  desorption  PTR-MS, Atmospheric  Measurement 621      Techniques, 7, 225-239, 10.5194/amt-7-225-2014, 2014.

622      Gentner, D. R., Isaacman, G., Worton, D. R., Chan, A. W., Dallmann, T. R., Davis, L.,

623  Liu, S., Day, D. A., Russell, L. M., Wilson, K. R., Weber, R., Guha, A., Harley, R. A., 624  and Goldstein, A. H.: Elucidating secondary organic aerosol from diesel and gasoline   625  vehicles through detailed characterization of organic carbon emissions, Proc Natl Acad 626       Sci U S A, 109, 18318-18323, 10.1073/pnas.1212272109, 2012.

627  Gentner, D. R., Worton, D. R., Isaacman, G., Davis, L. C., Dallmann, T. R., Wood, E.  628 C., Herndon, S. C., Goldstein, A. H., and Harley, R. A.: Chemical Composition of Gas- 629    Phase Organic Carbon Emissions from Motor Vehicles  and Implications for Ozone    630       Production,      Environmental      Science      &      Technology,      47,   11837-11848,

631       10.1021/es401470e, 2013.

632       Gentner, D. R., Jathar, S. H., Gordon, T.  D., Bahreini, R., Day, D. A., El Haddad,    I.,

633  Hayes, P.  L., Pieber, S. M., Platt, S. M., de Gouw, J., Goldstein, A. H., Harley, R. A.,   634 Jimenez, J. L., Prevot, A. S., and Robinson, A. L.: Review of Urban Secondary Organic 635   Aerosol Formation from Gasoline and Diesel Motor Vehicle Emissions, Environ Sci    636       Technol, 51, 1074-1093, 10.1021/acs.est.6b04509, 2017.

637  George, I. J., Hays, M. D., Herrington, J. S., Preston, W., Snow, R., Faircloth, J., George, 638 B. J., Long, T., and Baldauf, R. W.: Effects of Cold Temperature and Ethanol Content  639 on VOC  Emissions  from  Light-Duty  Gasoline Vehicles,  Environ  Sci Technol,  49,  640       13067-13074, 10.1021/acs.est.5b04102, 2015.

641 Guo, H., Zou, S. C., Tsai, W. Y., Chan, L. Y., and Blake, D. R.: Emission characteristics 642 of nonmethane hydrocarbons from private cars and taxis at different driving speeds in  643      Hong	Kong,	Atmospheric	Environment,	45,	2711-2721,

644      10.1016/j.atmosenv.2011.02.053, 2011.

645    Han, C., Liu, R., Luo, H., Li, G., Ma, S., Chen, J., and An, T.:  Pollution profiles of    646 volatile organic compounds from different urban functional areas in Guangzhou China 647   based  on  GC/MS  and  PTR-TOF-MS:  Atmospheric  environmental  implications,    648      Atmospheric Environment, 214, 10.1016/j.atmosenv.2019.116843, 2019.

649           He, X., Yuan,  B., Wu, C., Wang, S., Wang, C., Huangfu, Y.,  Qi, J., Ma, N., Xu, W.,

650  Wang, M., Chen, W., Su, H., Cheng, Y., and Shao, M.: Volatile organic compounds in   651  wintertime North China Plain: Insights from measurements of proton transfer reaction 652 time-of-flight mass spectrometer (PTR-ToF-MS), Journal of Environmental Sciences,  653       10.1016/j.jes.2021.08.010, 2022.

654    Huang,  J., Yuan,  Z.,  Duan, Y.,  Liu,  D.,  Fu,  Q.,  Liang,  G.,  Li,  F.,  and  Huang,  X.: 655    Quantification  of  temperature  dependence  of  vehicle  evaporative  volatile  organic 656 compound emissions from different fuel types in China, Sci Total Environ, 813, 152661, 657      10.1016/j.scitotenv.2021.152661, 2021.

658	http://e.jmrb.com/m/2008/11/17/10/m_182226.shtml, Access on 2009-12-10, 2008. 659	Kansal, A.: Sources and reactivity of NMHCs and VOCs in the atmosphere: a review, 660	J Hazard Mater, 166, 17-26, 10.1016/j.jhazmat.2008.11.048, 2009.

661  Koss, A. R., Sekimoto, K., Gilman, J. B., Selimovic, V., Coggon, M. M., Zarzana, K.  662  J., Yuan, B., Lerner, B. M., Brown, S. S., Jimenez, J. L., Krechmer, J., Roberts, J. M.,  663   Warneke, C., Yokelson, R. J., and de Gouw,  J.: Non-methane organic gas emissions    664  from biomass burning: identification, quantification, and emission factors from PTR-  665  ToF  during  the  FIREX  2016  laboratory  experiment,  Atmospheric  Chemistry  and 666       Physics, 18, 3299-3319, 10.5194/acp-18-3299-2018, 2018.

667 Kroll, J. H., Donahue, N. M., Jimenez, J. L., Kessler, S. H., Canagaratna, M. R., Wilson, 668 K. R., Altieri, K. E., Mazzoleni, L. R., Wozniak, A. S., Bluhm, H., Mysak, E. R., Smith, 669  J. D., Kolb, C. E., and Worsnop, D. R.: Carbon oxidation state as a metric for describing

670       the    chemistry    of    atmospheric    organic    aerosol,    Nat    Chem,    3,    133-139,

671      10.1038/nchem.948, 2011.

672 Kumar, A., Sinha, V., Shabin, M., Hakkim, H., Bonsang, B., and Gros, V.: Non-methane 673 hydrocarbon (NMHC) fingerprints of major urban and agricultural emission sources for 674  use in source apportionment studies, Atmospheric Chemistry and Physics, 20, 12133-  675       12152, 10.5194/acp-20-12133-2020, 2020.

676       Laurikko, J.: Ambient temperature effect on automotive exhaust emissions: FTP   and

677       ECE test cycle responses, The Science of Envioment, 169, 195-204, 1995.

678	Li, B., Ho, S. S. H., Xue, Y., Huang, Y., Wang, L., Cheng, Y., Dai, W., Zhong, H., Cao, 679	J., and Lee, S.: Characterizations of volatile organic compounds (VOCs) from vehicular 680	emissions  at  roadside  environment: The  first comprehensive  study in Northwestern 681	China, Atmospheric Environment, 161, 1-12, 10.1016/j.atmosenv.2017.04.029, 2017. 682	Li, T., Wang, Z., Yuan, B., Ye, C., Lin, Y., Wang, S., Sha, Q. e., Yuan, Z., Zheng, J., and 683	Shao, M.: Emissions of carboxylic acids, hydrogen cyanide (HCN) and isocyanic acid 684	(HNCO)	from	vehicle	exhaust,	Atmospheric	Environment, 685	10.1016/j.atmosenv.2021.118218, 2021.

686   Li, X., Wu, Y., Yao, X., Zhang, S., Zhou, Y., and Fu, L.: Evaluation of the environmental 687    benefits of the enhanced vehicle inspection /maintenance program based on the short   688 transient loaded mode in Guangzhou (in Chinese), Acta Scientiae Circumstantiae, 32(1), 689       101-108, 10.13671/j.hjkxxb.2012.01.009, 2012.

690  Liao, S., Zhang, J., Yu, F., Zhu, M., Liu, J., Ou, J., Dong, H., Sha, Q., Zhong, Z., Xie,  691  Y., Luo, H., Zhang, L., and Zheng, J.: High Gaseous Nitrous Acid (HONO) Emissions 692    from    Light-Duty    Diesel    Vehicles,    Environ    Sci    Technol,    55,    200-208,    693       10.1021/acs.est.0c05599, 2021.

694  Liu, H., Man, H., Cui, H., Wang, Y., Deng, F., Wang, Y., Yang, X., Xiao, Q., Zhang, Q., 695 Ding, Y., and He, K.: An updated emission inventory of vehicular VOCs and IVOCs in 696      China, Atmospheric Chemistry and Physics, 17, 12709-12724, 10.5194/acp-17-12709-

697       2017, 2017.

698    Liu, Y.,  Shao, M., Fu, L., Lu, S., Zeng, L., and Tang, D.: Source profiles of volatile    699  organic compounds (VOCs) measured in China: Part I, Atmospheric Environment, 42, 700      6247-6260, 10.1016/j.atmosenv.2008.01.070, 2008.

701       Liu, Y., Li, Y., Yuan, Z., Wang, H., Sha, Q., Lou, S., Liu, Y., Hao, Y., Duan, L., Ye,   P.,

702  Zheng, J., Yuan, B., and Shao, M.: Identification of two main origins of intermediate-  703 volatility  organic  compound  emissions  from  vehicles  in  China  through  two-phase 704       simultaneous         characterization,         Environ         Pollut,         281,           117020,

705      10.1016/j.envpol.2021.117020, 2021.

706  Lu, Q., Zhao, Y.,  and Robinson, A. L.: Comprehensive organic emission profiles for   707  gasoline,  diesel,  and  gas-turbine  engines  including  intermediate  and  semi-volatile 708 organic compound emissions, Atmospheric Chemistry and Physics, 18, 17637-17654,  709       10.5194/acp-18-17637-2018, 2018.

710   Ly, B. T., Kajii, Y., Nguyen, T. Y., Shoji, K., Van, D. A., Do, T. N., Nghiem, T. D., and 711  Sakamoto, Y.: Characteristics of roadside volatile organic compounds in an urban area 712    dominated by gasoline vehicles, a case study in Hanoi, Chemosphere, 254, 126749,    713       10.1016/j.chemosphere.2020.126749, 2020.

714   Lyu,  M., Bao, X., Zhu, R., and Matthews, R.: State-of-the-art outlook for light-duty   715  vehicle emission control standards and technologies in China, Clean Technologies and 716      Environmental Policy, 22, 757-771, 10.1007/s10098-020-01834-x, 2020.

717  May, A. A., Nguyen, N. T.,  Presto, A. A., Gordon, T.  D., Lipsky,  E. M., Karve, M.,   718 Gutierrez, A., Robertson, W. H., Zhang, M., Brandow, C., Chang, O., Chen, S., Cicero- 719      Fernandez, P., Dinkins, L., Fuentes, M., Huang, S.-M., Ling, R., Long, J., Maddox, C.,

720  Massetti, J., McCauley, E., Miguel, A., Na, K., Ong, R., Pang, Y.,  Rieger, P., Sax, T.,   721  Truong, T., Vo, T., Chattopadhyay, S., Maldonado, H., Maricq, M. M., and Robinson,   722   A. L.: Gas- and particle-phase primary emissions from in-use, on-road gasoline and    723      diesel	vehicles,          Atmospheric	Environment,	88,	247-260,

724      10.1016/j.atmosenv.2014.01.046, 2014.

725       China      Mobile      Source      Environmental      Management      Annual       Report:

726     http://www.mee.gov.cn/hjzl/sthjzk/ydyhjgl/201909/P020190905586230826402.pdf,

727      2019.

728 Mo, Z., Shao, M., and Lu, S.: Compilation of a source profile database for hydrocarbon 729   and   OVOC   emissions   in   China,   Atmospheric   Environment,   143,   209-217,   730      10.1016/j.atmosenv.2016.08.025, 2016.

731  Ou, J., Zheng, J., Li, R., Huang, X., Zhong, Z., Zhong, L., and Lin, H.: Speciated OVOC 732 and VOC emission inventories and their implications for reactivity-based ozone control 733  strategy in the Pearl River Delta region, China, Sci Total Environ, 530-531, 393-402,   734      10.1016/j.scitotenv.2015.05.062, 2015.

735    Pang, X., Mu, Y.,  Yuan,  J., and He, H.: Carbonyls emission from ethanol-blended     736  gasoline and biodiesel-ethanol-diesel used in engines, Atmospheric Environment, 42,  737      1349-1358, 10.1016/j.atmosenv.2007.10.075, 2008.

738   Parrish, D. D., Kuster, W.  C., Shao, M., Yokouchi, Y.,  Kondo, Y.,  Goldan, P.  D., de    739  Gouw, J. A., Koike, M., and Shirai, T.: Comparison of air pollutant emissions among   740      mega-cities,	Atmospheric	Environment,	43,	6435-6441,

741      10.1016/j.atmosenv.2009.06.024, 2009.

742  Qi, L., Liu, H., Shen, X., Fu, M., Huang, F., Man, H., Deng, F., Shaikh, A. A., Wang,  743 X.,  Dong,  R.,  Song,  C.,  and  He,  K.:  Intermediate-Volatility  Organic  Compound  744  Emissions from Nonroad Construction Machinery under Different Operation Modes,   745       Environ Sci Technol, 53, 13832-13840, 10.1021/acs.est.9b01316, 2019.

746  Qiao, Y. Z., Wang, H. L., Huang, C., Chen, C. H., and Huang, H. Y.: Source profile and 747   chemical reactivity of volatile organic compounds from vehicle exhaust(in chinese),   748       Environmental Science, 33, 1071-1079, 2012.

749 Roy, A., Sonntag, D., Cook, R., Yanca, C., Schenk, C., and Choi, Y.: Effect of Ambient 750  Temperature  on  Total  Organic  Gas  Speciation  Profiles  from  Light-Duty  Gasoline 751       Vehicle     Exhaust,    Environmental    Science    &    Technology,     50,    6565-6573,

752       10.1021/acs.est.6b01081, 2016.

753 Rubin, J. I., Kean, A. J., Harley, R. A., Millet, D. B., and Goldstein, A. H.: Temperature 754  dependence of volatile organic compound evaporative emissions from motor vehicles, 755      Journal	of	Geophysical	Research:	Atmospheres,	111, 756      https://doi.org/10.1029/2005JD006458, 2006.

757   Schauer, J. J., Kleeman, M. J., Cass, G. R., and Simoneit, B. R., T.: Measurement of   758    Emissions from Air Pollution Sources. 2. C1 through C30 Organic Compounds from    759  Medium Duty Diesel Trucks, Environmental Science & Technology, 33, 1578-1587,   760      1999.

761       Seinfeld,  J.  H.,  and  Pandis,  S.  N.:  Atmospheric  chemistry  and  physics:  from air

762       pollution to climate change, John Wiley & Sons, Inc., Hoboken, 2006.

763  Sekimoto, K., Li, S.-M., Yuan, B., Koss, A., Coggon, M., Warneke, C., and de Gouw,  764  J.: Calculation of the sensitivity of proton-transfer-reaction mass spectrometry (PTR-   765  MS) for organic trace gases using molecular properties, International Journal of Mass  766      Spectrometry, 421, 71-94, 10.1016/j.ijms.2017.04.006, 2017.

767      Sha, Q., Zhu, M., Huang, H., Wang, Y., Huang, Z., Zhang, X., Tang, M., Lu, M., Chen,

768    C., Shi, B., Chen, Z., Wu, L., Zhong, Z., Li, C., Xu, Y., Yu, F., Jia, G., Liao, S., Cui, X.,

769  Liu, J., and Zheng, J.: A newly integrated dataset of volatile organic compounds (VOCs) 770 source profiles and implications for the future development of VOCs profiles in China, 771      Sci Total Environ, 793, 148348, 10.1016/j.scitotenv.2021.148348, 2021.

772  Shao, M., Zhang, Y., Zeng, L., Tang, X., Zhang, J., Zhong, L., and Wang, B.: Ground- 773  level ozone in the Pearl River Delta and the roles of VOC and NOx in its production,   774      Journal of Environmental Management, 90, 512-518, 10.1016/j.jenvman.2007.12.008,

775      2009.

776  Shen, X., Lv, T., Zhang, X., Cao, X., Li, X., Wu, B., Yao, X., Shi, Y., Zhou, Q., Chen,  777 X., and Yao, Z.: Real-world emission characteristics of black carbon emitted by on-road 778  China IV and China V diesel trucks, Science of The Total Environment, 799, 149435, 779      https://doi.org/10.1016/j.scitotenv.2021.149435, 2021.

780      Song, C., Liu, Y.,  Sun, L., Zhang, Q., and Mao, H.: Emissions of volatile organic      781   compounds (VOCs) from gasoline- and liquified natural gas (LNG)-fueled vehicles in 782 tunnel studies, Atmospheric Environment, 234, 10.1016/j.atmosenv.2020.117626, 2020. 783  Stark, H., Yatavelli, R. L. N., Thompson, S. L., Kimmel, J. R., Cubison, M. J., Chhabra, 784   P. S., Canagaratna, M. R., Jayne, J. T., Worsnop, D. R., and Jimenez, J. L.: Methods to 785   extract molecular and bulk chemical information from series of complex mass spectra 786  with limited mass resolution, International Journal of Mass Spectrometry, 389, 26-38,  787      10.1016/j.ijms.2015.08.011, 2015.

788 Sulzer, P., Hartungen, E., Hanel, G., Feil, S., Winkler, K., Mutschlechner, P., Haidacher, 789 S., Schottkowsky, R., Gunsch, D., Seehauser, H., Striednig, M., Jürschik, S., Breiev, K., 790 Lanza,  M.,  Herbig,  J.,  Märk,  L.,  Märk,  T.  D.,  and  Jordan, A.: A  Proton  Transfer 791 Reaction-Quadrupole  interface  Time-Of-Flight  Mass  Spectrometer  (PTR-QiTOF):  792 High speed due to extreme sensitivity, International Journal of Mass Spectrometry, 368, 793       1-5, 10.1016/j.ijms.2014.05.004, 2014.

794  Sun, W., Shao, M., Granier, C., Liu, Y., Ye, C. S., and Zheng, J. Y.: Long-Term Trends 795 of Anthropogenic SO2, NOx, CO, and NMVOCs Emissions in China, Earth's Future, 6, 796      1112-1133, 10.1029/2018ef000822, 2018.

797    Tsai,  J.-H., Chang, S.-Y.,  and Chiang, H.-L.: Volatile  organic compounds from the    798  exhaust  of   light-duty   diesel   vehicles,  Atmospheric   Environment,   61,   499-506, 799      10.1016/j.atmosenv.2012.07.078, 2012.

800       Wallington, T.  J., Lambert, C. K., and Ruona, W.  C.: Diesel vehicles and  sustainable

801    mobility in the U.S, Energy Policy, 54, 47-53, 10.1016/j.enpol.2011.11.068, 2013.

802       Wang, C., Yuan, B., Wu, C., Wang, S., Qi, J., Wang, B., Wang, Z., Hu, W.,    Chen, W.,

803       Ye, C., Wang, W., Sun, Y., Wang, C., Huang, S., Song, W., Wang, X., Yang, S., Zhang,

804   S., Xu, W., Ma, N., Zhang, Z., Jiang, B., Su, H., Cheng, Y., Wang, X., and Shao, M.:   805  Measurements  of  higher  alkanes  using  NO+  chemical  ionization  in  PTR-ToF-MS: 806  important contributions  of  higher alkanes to  secondary  organic aerosols  in  China,   807      Atmospheric Chemistry and Physics, 20, 14123-14138,  10.5194/acp-20-14123-2020,

808      2020a.

809  Wang, H., L. , Jing, S., A. , Lou, S., R. , Hu, Q., Y. , Li, L., Tao, S., K. , Huang, C., Qiao,

810   L., P.  , and Chen, C., H.: Volatile organic compounds (VOCs) source profiles of on-   811   road   vehicle    emissions    in    China,    Sci    Total    Environ,    607-608,    253-261, 812      10.1016/j.scitotenv.2017.07.001, 2017.

813     Wang,  J., Jin, L., Gao, J., Shi, J., Zhao, Y.,  Liu, S., Jin, T.,  Bai, Z., and Wu,  C. Y.:     814    Investigation of speciated VOC in gasoline vehicular exhaust under ECE and EUDC   815 test cycles, Sci Total Environ, 445-446, 110-116, 10.1016/j.scitotenv.2012.12.044, 2013. 816    Wang, M., Li, S., Zhu, R., Zhang, R., Zu, L., Wang, Y., and Bao, X.: On-road tailpipe  817   emission characteristics and ozone formation potentials of VOCs from gasoline, diesel 818    and    liquefied    petroleum    gas    fueled    vehicles,    Atmospheric    Environment,  819      10.1016/j.atmosenv.2020.117294, 2020b.

820       Wang, Z., Yuan, B., Ye, C., Roberts, J., Wisthaler, A., Lin, Y., Li, T., Wu, C., Peng,  Y.,

821       Wang, C., Wang, S., Yang, S., Wang, B., Qi, J., Wang, C., Song, W., Hu, W., Wang, X.,

822  Xu, W., Ma, N., Kuang, Y., Tao, J., Zhang, Z., Su, H., Cheng, Y., Wang, X., and Shao,  823  M.:  High  Concentrations  of Atmospheric  Isocyanic Acid  (HNCO)  Produced  from 824    Secondary    Sources     in     China,     Environmental     Science     &     Technology,  825       10.1021/acs.est.0c02843, 2020c.

826    Wu, C., Wang, C., Wang, S., Wang, W., Yuan, B., Qi, J., Wang, B., Wang, H., Wang, C.,

827   Song, W., Wang, X., Hu, W., Lou, S., Ye, C., Peng, Y., Wang, Z., Huangfu, Y., Xie, Y., 828 Zhu, M., Zheng, J., Wang, X., Jiang, B., Zhang, Z., and Shao, M.: Measurement report: 829  Important  contributions  of  oxygenated  compounds  to  emissions  and  chemistry  of 830     volatile organic compounds in urban air, Atmospheric Chemistry and Physics, 20,     831       14769-14785, 10.5194/acp-20-14769-2020, 2020.

832    Wu,  R., Bo, Y.,  Li, J., Li, L., Li, Y.,  and Xie, S.: Method to establish the emission     833  inventory of anthropogenic volatile organic compounds in China and its application in 834       the       period       2008–2012,      Atmospheric       Environment,       127,     244-254,

835      10.1016/j.atmosenv.2015.12.015, 2016.

836   Wu, Y.,  Zhang, S., Hao, J., Liu, H., Wu,  X., Hu, J., Walsh,  M. P.,  Wallington, T.  J.,   837  Zhang, K. M., and Stevanovic, S.: On-road vehicle emissions and their control in China: 838      A      review      and       outlook,       Sci       Total       Environ,       574,       332-349, 839      10.1016/j.scitotenv.2016.09.040, 2017.

840   Yang,   W.,   Zhang,  Q.,  Wang,   J.,  Zhou,  C.,  Zhang,  Y.,   and  Pan,  Z.:  Emission   841  characteristics and ozone formation potentials of VOCs from gasoline passenger cars  842   at    different    driving    modes,   Atmospheric    Pollution    Research,    9,    804-813, 843      10.1016/j.apr.2018.01.002, 2018.

844 Yao,  S.,  Liu,  Z.,  and  Qi,  Z.: Test  System  for  Exhaust  Pollutants  from  Light-duty 845   Gasoline  Vehicle  under  Short  Transient  Driving  Cycle  (in  Chinese),  Shanghai    846       Environmental Sciences, 10, 722-728, 2003.

847   Yao, Z., Shen, X., Ye, Y., Cao, X., Jiang, X., Zhang, Y., and He, K.: On-road emission  848 characteristics of VOCs from diesel trucks in Beijing, China, Atmospheric Environment, 849      103, 87-93, 10.1016/j.atmosenv.2014.12.028, 2015.

850      Ye, C., Yuan, B., Lin, Y., Wang, Z., Hu, W., Li, T., Chen, W., Wu, C., Wang, C., Huang,

851   S., Qi, J., Wang, B., Wang, C., Song, W., Wang, X., Zheng, E., Krechmer, J. E., Ye, P., 852  Zhang,  Z., Wang,  X., Worsnop,  D.  R.,  and  Shao,  M.:  Chemical characterization of 853  oxygenated organic compounds in the gas phase and particle phase using iodide CIMS 854    with FIGAERO in urban air, Atmospheric Chemistry and Physics, 21, 8455-8478,     855       10.5194/acp-21-8455-2021, 2021.

856   Yuan, B., Koss, A. R., Warneke, C., Coggon, M., Sekimoto, K., and de Gouw, J. A.:    857 Proton-Transfer-Reaction Mass Spectrometry: Applications in Atmospheric Sciences,  858      Chemical Reviews, 117, 13187-13229, 10.1021/acs.chemrev.7b00325, 2017.

859   Yue,  X., Wu, Y.,  Hao, J., Pang, Y.,  Ma, Y.,  Li, Y.,  Li, B., and Bao, X.: Fuel quality    860    management  versus  vehicle  emission  control  in  China,  status  quo  and  future     861      perspectives,  Energy  Policy,  79,  87-98, https://doi.org/10.1016/j.enpol.2015.01.009,

862      2015.

863      Zavala, M., Herndon, S. C., Slott, R. S., Dunlea, E. J., Marr, L. C., Shorter, J. H.,      864  Zahniser, M., Knighton, W. B., Rogers, T. M., Kolb, C. E., Molina, L. T., and Molina,  865  M. J.: Characterization of on-road vehicle emissions in the Mexico City Metropolitan  866   Area using a mobile laboratory in chase and fleet average measurement modes during 867  the MCMA-2003 field campaign, Atmospheric Chemistry and Physics, 6, 5129-5142, 868       10.5194/acp-6-5129-2006, 2006.

869  Zavala, M., Herndon, S. C., Wood, E. C., Jayne, J. T., Nelson, D. D., Trimborn, A. M., 870 Dunlea, E., Knighton, W. B., Mendoza, A., Allen, D. T., Kolb, C. E., Molina, M. J., and 871 Molina, L. T.: Comparison of emissions from on-road sources using a mobile laboratory 872   under various driving and operational sampling modes, Atmospheric Chemistry and   873       Physics, 9, 1-14, 10.5194/acp-9-1-2009, 2009.

874      Zhang, Q., Wu,  L., Fang, X., Liu,  M., Zhang, J., Shao, M., Lu, S., and Mao, H.:      875 Emission factors of volatile organic compounds (VOCs) based on the detailed vehicle  876    classification    in     a     tunnel     study,     Sci     Total     Environ,     624,     878-886, 877      10.1016/j.scitotenv.2017.12.171, 2018.

878 Zhao, Y., Saleh, R., Saliba, G., Presto, A. A., Gordon, T. D., Drozd, G. T., Goldstein, A. 879  H.,  Donahue,  N.  M.,  and  Robinson,  A.  L.:  Reducing  secondary  organic  aerosol 880  formation from gasoline vehicle exhaust, Proc Natl Acad Sci U S A, 114, 6984-6989,  881      10.1073/pnas.1620911114, 2017.

882  Zhou, H., Zhao, H., Hu, J., Li, M., Feng, Q., Qi, J., Shi, Z., Mao, H., and Jin, T.: Primary 883     particulate matter emissions and estimates of secondary organic aerosol formation     884 potential from the exhaust of a China V diesel engine, Atmospheric Environment, 218, 885      116987, https://doi.org/10.1016/j.atmosenv.2019.116987, 2019.

886       Zhu, M., Dong, H., Yu, F., Liao, S., Xie, Y., Liu, J., Sha, Q., Zhong, Z., Zeng, L.,  and

887      Zheng,  J.: A New  Portable  Instrument  for  Online  Measurements of Formaldehyde:

888	From Ambient to Mobile Emission Sources, Environmental Science & Technology

889	Letters, 7, 292-297, 10.1021/acs.estlett.0c00169, 2020.

890	Ziemann, P. J., and Atkinson, R.: Kinetics, products, and mechanisms of secondary

891	organic aerosol formation, Chem Soc Rev, 41, 6582-6605, 10.1039/c2cs35122f, 2012.

892

893

894

895    Figure 1. Real-time concentrations of acetaldehyde, acetone, benzene, toluene, and    896   CO2 for (a) a gasoline vehicle with emission standard of China I and (b) a light-duty    897 diesel vehicle (LDDV) with emission standard of China IV. The two vehicles were both 898      cold started. The gray shadows represent the speed of the vehicles on the chassis      899      dynamometer.

900

901

902   Figure 2. The determined average mileage-based emission factors (mg·km-1) for (a)    903     benzene, (b) toluene, (c) acetaldehyde, and (d) acetone for vehicles with different      904 emission  standards.  The  numbers  above  the  top  axis  represent  the  number  of  all 905    experiments (including multiple measurements for individual test vehicle) for each     906  emission standard. LDDT, MDDT, HDDT, and BUS represent light-duty-diesel-truck, 907 middle-duty-diesel-truck,  heavy-duty-diesel-truck,  and  bus,  respectively.  Error  bars 908      represent standard deviations of emission factors for the specific emission standard.

909

910

911    Figure 3. Scatterplot of the emission factor of toluene in (a) gasoline and (b) diesel    912  vehicles, and acetone in (c) gasoline and (d) diesel vehicles during the hot start based   913      on the odometer for each vehicle.

914

915

916      Figure 4. The determined emission factors of representative OVOC species from      917    different types of vehicles. Error bars represent standard deviations of the emission     918       factors for the VOCs.

919

920

921    Figure 5. The determined average mileage-based emission factors of VOC species     922   measured by PTR-ToF-MS from (a) gasoline, (b) diesel, and (c) LPG vehicles. The    923      gray dashed lines represent 1‰ of total VOCs emission factors.

924

925

926	Figure 6.  The two-dimensional space of   -𝑺-𝑪- - 𝒏𝑪 with data points sized coded using

927  emission factors of VOC species from (a) gasoline and (b) diesel vehicles, and (c) the  928 ratio of emission factors of diesel vehicle relative to gasoline vehicle. The black and 929       gray lines are the average -𝑶-𝑺-𝑪- of each carbon number for VOC species in gasoline and

930      diesel vehicles,  respectively.

931

932

933   Figure 7. Scatterplots of VOCs emission factors between cold start and hot start for    934    gasoline (a) and diesel vehicles (b). Scatterplots of VOCs emission factors between    935 China I and China V emission standard for gasoline vehicles (c) and between China III 936 and China V emission standard for diesel vehicles (d). Each data point indicates a VOC 937     species measured by PTR-ToF-MS. The blue lines are the fitted results for all data     938  points. The black dashed lines represent 1:1 ratio, and the shaded areas represent ratios 939       of a factor of 2 in (a) and (b), and a factor of 10 and 100 in (c) and (d).

940

941

942  Figure 8. Scatterplot of VOCs emission factors between gasoline and diesel vehicles. 943  Each data point indicates a VOC species measured by PTR-ToF-MS. The blue line is  944  the fitted result for all data points. The black line represents 1:1 ratio, and the shaded   945       areas represent ratios of a factor of 10 and 100.

946

947

948  Figure 9. The determined emission factors of (a) aromatics and (b) carbonyls for each 949  carbon  number  from  gasoline  and  diesel  vehicles.  Error  bars  represent  standard  950      deviations of the emission factors for the VOCs of different carbon number.

951

952

953  Figure  10.  Scatterplots  of  the  determined  mileage-based  emission  factors  of  (a) 954     benzene versus toluene, (b) C14 aromatics versus toluene, (c) formaldehyde versus     955 toluene, and (d) acetaldehyde versus toluene for gasoline and diesel vehicles. Each data 956 point represents each test vehicle in this study. The green and orange lines are the fitted 957     results for gasoline and diesel vehicle. The black line represents 1:1 ratio, and the      958  shaded areas represent ratio of a factor of 10. The green and orange line are the fits to  959   gasoline and diesel points in each plot. Note that these linear fits are shown in curves  960       in log-log space as the result of non-zero y-intercept.

961

962

963 Figure 11. (a) The determined average emission factors for different emission standard 964  from gasoline, diesel (×0.5), and LPG (×100) vehicles measured by PTR-ToF-MS. The 965   different ion categories are discussed in the manuscript. Fractions of the determined    966 average emission factors of VOCs ions in different ion categories from (b) gasoline, (c) 967  diesel, and (d) LPG vehicles. The numbers above the top axis represent the number of 968  all experiments (including multiple measurements for individual test vehicle) for each 969      emission standard.

970

971

972

973     Figure 12. Comparison of OVOCs fractions determined in this study and those in     974  previous studies. Error bars represent the standard deviations of the weight percentage 975   of OVOCs.  The C, E, A, M above the top axis represent the four groups of OVOCs   976     measured in this study or previous studies, including Carbonyl: C, Ester/Ether: E,      977       Alcohol: A, Multiple-functional: M.

# Comments

Are these the 2 aromatics you mean?

# Text boxes

-1	-1